PCIe 4S (16C950 128 FIFO)

User Manual		 English

LINDY No. 51189

#### www.lindy.com

Introduction

Thank you for purchasing the LINDY PCIe four Port Serial. This card is equipped with one high speed RS-232 serial interfaces.

The serial ports include 128Byte FIFO with speeds up to 921Kb/Sec.

Port Specification

Serial Port:

- Chipset: Oxford OXPCIe954, 128Byte DMA FIFO

- Compatible chips: with 16C950, 16C750, 16C650, 16C550, and 16C450.

- IEEE standard: RS-232 Interface

- Max. Speed: Bi-directional speeds from 50 bps to 15Mbps/port.

- 1 x DB44 Female

Package Contents

- 1 x LINDY PCIe 4S Card

- LINDY User manual

- LINDY Driver CD

- LINDY cable 4 x DB9 Male

Installation

- Turn off the power of your computer and remove the power cable

- Install the PCI card into an available PCI slot in your computer

- Connect the peripheral ie Printer, Modem, etc. to the adapters port

- Re-connect the power cable & turn on the power of your computer

PCI device listing display (for example…)

| Bus No | Device No | Func No | Vendor ID | Device ID | Device Class | IRQ |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 7 | 1 | 8086 | 7010 | IDE Controller | 14 |
| 0 | 13 | 0 | 1409 | 7168 | Simple COMM. Controller | 10 |

If the Vendor ID, Device ID, Device Class or IRQ aren’t displayed or an error occurs, please try another PCI slot.

Once the hardware has installed correctly you can start installing the software from the driver CD.

Pin Assignments

Serial 9 Pin male connector pin assignments:

| Serial 9 Pin male connector : |
| --- |
| Pin | Signal | Pin | Signal | Pin | Signal | Pin | Signal |
| 1 | CD | 4 | DTR | 6 | DSR | 8 | CTS |
| 2 | RD | 5 | GROUND | 7 | RTS | 9 | RI |
| 3 | TD |  |

Technical Specifications

- 4 independent RS-232 serial ports with communication speeds up to 230（921）Kbps

- Designed to meet PCI-Express Base Specification Revision 1.1

- Supports x1,x2,x4,x8,x16（lane）PCI-Express Bus connector keys

- High speed 16C950 compatible UART controller on-board

- On-chip hardware auto flow control to guarantee no data loss

- Built-in 128K byte DMA software FIFO

- Certified by Microsoft WHQL,CE,FCC approval

- Support DOS,Linux,Microsoft Windows 2000/XP/2003 and Vista

- Ready of the Intel and AMD 32/64-bit CPU System

Certifications

FCC Certifications

This equipment has been tested and found to comply with the limits for a Class A digital device, pursuant to part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference when the equipment is operated in a commercial environment. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instruction manual, may cause harmful interference to radio communications. Operation of this equipment in a residential area is likely to cause harmful interference in which case the user will be required to correct the interference at their own expense.

This device complies with Part 15 of the FCC Rules. Operation is subject to the following two conditions: (1) this device may not cause harmful interference, and (2) this device must accept any interference received; including interference that may cause undesired operation.

CE Certification

This equipment complies with the requirements relating to electromagnetic compatibility, EN 55024 and EN55022 class A for ITE, EN61000-3-2/-3 the essential protection requirement of Council Directive 89/336/EEC on the approximation of the laws of the Member States relating to electromagnetic compatibility.

Recycling Information

WEEE (Waste of Electrical and Electronic Equipment), 
Recycling of Electronic Products

United Kingdom

In 2006 the European Union introduced regulations (WEEE) for the collection and recycling of all waste electrical and electronic equipment. It is no longer allowable to simply throw away electrical and electronic equipment. Instead, these products must enter the recycling process.

Each individual EU member state has implemented the WEEE regulations into national law in slightly different ways. Please follow your national law when you want to dispose of any electrical or electronic products. More details can be obtained from your national WEEE recycling agency.

Germany / Deutschland

Die Europäische Union hat mit der WEEE Direktive umfassende Regelungen für die Verschrottung und das Recycling von Elektro- und Elektronikprodukten geschaffen. Diese wurden von der Bundesregierung im Elektro- und Elektronikgerätegesetz – ElektroG in deutsches Recht umgesetzt. Dieses Gesetz verbietet vom 24.März 2006 an das Entsorgen von entsprechenden, auch alten, Elektro- und Elektronikgeräten über die Hausmülltonne! Diese Geräte  müssen den lokalen Sammelsystemen bzw. örtlichen Sammelstellen zugeführt werden! Dort werden sie kostenlos entgegen genommen. Die Kosten für den weiteren Recyclingprozess übernimmt die Gesamtheit der Gerätehersteller.

France

En  2006, l'union Européenne a introduit  la nouvelle réglementation (WEEE) pour le recyclage de tout équipement électrique et électronique.

Chaque Etat membre de l’ Union Européenne a mis en application la nouvelle réglementation  WEEE  de manières légèrement différentes. Veuillez suivre le décret d’application correspondant à l’élimination des déchets électriques ou électroniques de votre pays.

Italy

Nel 2006 l’unione europea ha introdotto regolamentazioni (WEEE) per la raccolta e il riciclo di apparecchi elettrici ed elettronici. Non è più consentito semplicemente gettare queste apparecchiature, devono essere riciclate. Ogni stato membro dell’ EU ha tramutato le direttive WEEE in leggi statali in varie misure. Fare riferimento alle leggi del proprio Stato quando si dispone di un apparecchio elettrico o elettronico.

Per ulteriori dettagli fare riferimento alla direttiva  WEEE sul riciclaggio del proprio Stato.

LINDY No. 51189

www.lindy.com